## Slide 2
1. Convert .d to mzml using MSConvert
4. Give output path in “main.py” for csv output
6. Select mzml file to be analyzed in the popup
2. Run “setup_environment.py” (only run once, no need to run more than once)
3. Open “main.py” – scroll to bottom
5. Run “main.py”
7. Go to the output location – csv output should be there

## Slide 3: Using MSConvert
Convert .d into mzML
No filters are selected, just load in the data and hit start
https://proteowizard.sourceforge.io/download.html

## Slide 4: Pop up from the Main.py
Read in the mzml file into the script

## Slide 5
m/z | Retention Time (sec) | Drift Time (ms) | Intensity | Count
141.0159609 | 8.016101299 | 23.06790938 | 887799 | 770
Openms is able to extract features accurately – I then am implementing a clustering algorithm (DBSCAN) in which I am using some basic instrument parameters to determine clusters (the count in the csv). This is then able to be plotted into some very nice 3D plots.
I have applied a feature intensity threshold as I am using experimental samples and there is a lot of background.
Browser feature
CSV export
Number of points within the peak